## Slide 1
TERNARY KWS ACCELERATOR
Always-On Keyword Spotting on Silicon · ECE 410/510 · Spring 2026 · Manaf Alali
What Am I Doing?
Custom ASIC for 'Hey Alexa'-style keyword spotting on tiny IoT devices
Ternary weights: only −1, 0, +1 — no multipliers, pure adder logic
10-class Google Speech Commands, target <1 mW always-on
How's It Done?
Prior art: PyTorch on CPU/GPU — accurate but power-hungry & memory-bound
BNN/TNN accelerators (Rusci 2020): XNOR+popcount on ARM Cortex-M
Key: on-chip weight SRAM avoids DRAM bandwidth bottleneck
What Am I Doing Differently?
Roofline flip: AI 0.50 → 406 FLOP/byte (memory-bound → compute-bound)
Eliminates ALL multipliers — ternary MAC = pure adder tree, ~20× smaller
SPI slave interface; drop-in MCU integration; parametric SystemVerilog
Accomplished So Far
SW baseline: 4.91 GFLOP/s, 0.44 ms/inference, AI=0.50 confirmed
RTL done: compute_core.sv (ternary MAC) + spi_slave.sv (SPI Mode 0)
Both testbenches PASS: 4/4 MAC outputs + SPI write/read verified
What's Next?
M3: OpenLane 2 ASIC synthesis → real area, power & timing reports
M4: Benchmark HW vs. SW speedup for FC1 (target: >100×)
Success = synthesizable design, ≥92% KWS accuracy, <1 mW active
Roofline Analysis
4× smaller
weight storage
>100× target
speedup
FC1 kernel: 1960→512, 2M FLOPs, 251 KB ternary weights fit on-chip | github.com/alali1o/ECE-410